Metax
Get Algorithm

Version 0.1
Last modified on` 26.06.2018
Number of pages` 7
Document History
Date	Description	Author(s)
25-May-2018	Version 0.1: Initial version of the document	Garik

# Introduction
## About the document
This document describes the get algorithm of Metax.
## Terms, acronyms and abbreviations
Kernel – Layer in Metax architecture. It implements the core logic, like splitting files into chunks, generating shared/master objects, integrating files from pieces, deciding participation in tenders, etc.
Router – Performs routing of data between its own kernel to peers, or as an intermediate bridge for other peers
Link – Manages connections with peers
Storage – Stores files as key/value pairs. Can save file into hard drive with the given key (uuid) or retrieve file with the given key (uuid) from hard drive.
Key Manager – Generates and keeps track of users RSA keys and AES keys for data encryption. Performs all kind of encryption/decryption tasks.
## References
1. leviathan_whitepaper.odt
2. leviathan_system_overview.odt
3. metax_general_notes.txt
4. leviathan_metax_api.odt
# Get Algorithm in Kernel
TODO: Describe the rest of the get request.
## Streaming
### General Description
Metax supports streaming get request. Streaming means that Metax sends to the client the first chunk of the file as it is available in the Kernel, then the second one as it is available, etc., without waiting for the all chunks to be available in the Kernel.
Metax starts to stream the files if the “content_type” key is present in the shared object of the file and it contains “video” or “audio” keywords.
Below is the general flow of the streaming (if the requested uuid is the first time):
- Client: The user saves media file by specifying the content type via Metax-Content-Type header. E.g. if the file is an mp4 video then the value of the header should be “video/mp4”. There is now any other difference in save request for media types.
- Client: The user gets the file, e.g. via browser supporting html5.
- DB Request Handler: The db request handler processes it other get requests, e.g. forwards the request to IMS. Important details is that db handler passes client id to the IMS, which later will be used for cleanup purposes. As the ID db handler uses its pointer (this) converted to unsigned long int type.
- Vostan IMS: IMS processes the the request as ordinary get request: generates request_info object for keeping all necessary info about the get request, then passes the request to Kernel.
- Kernel: Kernel posts get request to storage or to router (if storage fails) for getting share object.
- Kernel: If the content type is set in the share object it is remembered in the request object. Then lookup for master object is sent to storage (or router if storage refuses).
- Kernel: After master object arrives, Kernel checks the requests content type. If it is media (video or audio) then the following steps are done:
  - Stream state is constructed for the streaming. A vector is created for each chunk of the file. The vector element contains the chunks uuid, start address in the file, its size, whether the chunk is already available in the kernel, the temporary file path of the chunk if it is available. The vector is sorted by the start address of the chunks. Note that the vector is stored in the request object as shared pointer, as all the requests for the same uuid share the same vector. In stream state object we keep track of the current chunk that should be sent to the client. At the beginning the current chunk is calculated on the range info received from the client, i.e. it is calculated from the based on the byte from which the client has requested the file. If no range specified by the client (the value of range start and length will -1 in this case) then the current chunk will be initialized to the first chunk (chunk number 0 in the vector).
  - Stream prepare message is sent to IMS.
  - IMS generates promise/future pairs for each chunk to be sent to the db handler and sends the list of futures to the db handler.
  - Db handler checks whether there is a future vector available from the IMS, if yes, then Metax is going to provide streaming (otherwise the whole file should be sent to the client). Db handler sets corresponding headers to the client response: “Accept-Ranges”, “Content-Range” if the request was a range.
  - Kernel sends lookup request for each chunk
- Kernel: As chunk arrives from storage or router kernel checks whether it is part of a streaming request, if yes, then the data is being written in a tmp file and the chunk is marked as available in the kernel. Then the chunk is being sent to IMS. The current chunk is increased to be the next chunk. Note, it is immediately checked whether the next chunks are available and in case of positive result they are all sent to IMS till the current will be set to chunk (or end of the vector) which is not yet available in the Kernel.
- Vostan IMS: As IMS receives chunk of a request which should be streamed it, the tmp file path value is being set to the corresponding promise object for that chunk.
- DB Request Handler: Db request handler as receives the chunk via future::get, reads chunk content from the tmp file and copies into the response object of the client.
- DB Request Handler: In the db handler if all the future objects corresponding to the chunks are handled, then sends stream cleanup request to IMS providing its pointer value (converted to unsigned long) to IMS as client ID.
- Vostan IMS: IMS as receives the stream cleanup request from db handler, cleans up all the containers, holding info about the request associated with the received client id and sends cleanup request to Kernel.
- Kernel: Kernel as receives cleanup request from the IMS, cleans up all the information about the corresponding request. Note, if the same file is being streamed also to other requests, than the chunk list will not be cleaned up until the last request is cleaned. This is achieved by storing the vector of the chunks as a shared pointer inside the request objects.
### Notes for DB Request handler
- Db handler provides a unique id to IMS for remembering the client ID. It is later is used for cleaning the request in IMS and Kernel associated with the client ID.
  “this” pointer is used as client id by converting it to unsigned long int.
- The client ID is not necessary for not streamed get requests, but at the time of receiving get request, it is not known whether the request will be streamed or not. That’s why it provides client ID to IMS for any get request.
- When the first response is received from the IMS to a request, db handler checks whether IMS provided a pointer to a vector with future objects. If it is provided then db handler is prepared for streaming, otherwise it just sends the information received from IMS at once to the client.
- The size of the future objects in the received list should correspond to the number of chunks IMS/Kernel is going to the send. Db request handler starts to call future::get method from the beginning of the list till the end. After the last future::get returned and the response is sent, db handler sends cleanup request to IMS and provides the client ID.
- When receiving get request db handler checks whether the “Range” header is provided by the client. If yes, then it parses the range and from the header and sends to IMS a pair: start and length. If the “Range” header isn’t provided then the range pair members are set to -1.
- DB request handler sets “Accept-Ranges: bytes” header to response, then the response should be streamed. This allows to clients like browsers which play audio/movie to enable seek functionality.
- When the request should be streamed, IMS provides also a range (pair of values). The second one is the length of the chunk and is used for setting the “Content-Length” header. If the first one is not -1 then “Content-Range: <start byte>-<end byte>/<length>” header is also being set to response. This means that client requested range range, and the first value from IMS should correspond to the start byte of the client request.
- There is a sleep (1 second) before sending cleanup request to IMS. It helps to improve performance in case of seek. When the user seeks the video, a new request is sent by client and the old one is cleaned. The sleep helps the new request to reach Kernel earlier than clean request, so that the new request can reuse already saved chunks from the old request.
### Notes for Vostan IMS
- When receives get request from db handler, generates request_info object and stores all necessary information for the request. Associates received client id with the request object.
- When receives metax::prepare_streaming message from Metax, it generates list of promise/future objects with the size received from Metax. The size is the expected number of chunks to be streamed
- Sends the future list to the db request handler.
- When receives response to get request from Metax, checks whether this response is a part of streaming by checking whether there is promise list generated for the request. If the received data is part of streaming sets it to the current element from the promise list and increases the current to point next promise object from the list.
### Notes for Kernel
- When receives get request from IMS checks whether the request uuid is already being processed by the kernel. If no then it posts share object lookup request to storage (or router if storage refuses). If yes, then it checks whether the request is streaming. If yes, then it constructs streaming state object by referring to the chunk list of already processed request. For the new request current chunk is calculated based on whether range is provided. If not the the 0 chunk is set as the current.
- The new request is added to the list of ongoing requests processing the uuid.
- Two streaming requests for the same uuid might arrive quickly one after another. In this case they are both added to the pending get requests list. As one of them receives master object and it is clear the get request is streaming and the streaming object is constructed, all other pending requests also are visited and their streaming state is constructed. The list of chunks is copied from the request who received the master object first.
- When a chunk arrives from storage or router, it is being written in the tmp file and the state of the chunk in the chunk list is updated by marking as available in the Kernel. Then all the pending request waiting for that chunk are processed and the chunk is sent to the IMS for all the pending requests.
- If the request has range and the start byte of a request lies inside the arrived chunk, then a new tmp file is constructed by cropping the first part of the chunk, so it is started from the byte received from range pair (first value).
- When cleanup request is received from IMS, it finds the Kernel finds the request object associated with the IMS request, finds the corresponding uuid from the request object, finds the corresponding entry for the request in the pending get requests list and removes it from there. If all the requests for the uuid are removed, the entry of the uuid in pending get requests is also removed. Note, the chunk list in the streaming state is kept as shared pointer. So it shared among all the requests for the particular uuid, but is removed automatically by the shared pointer’s destructor when the last stream request for the uuid is removed.