Metax
Key Transfer Algorithm

Version 0.2
Last modified on` 30.10.2019
Number of pages` 6
Document History
Date	Description	Author(s)
25-Oct-2019	Version 0.1: Initial version of the document	Marine
30-Oct-2019	Version 0.2: Updated Terms, Acronyms and Abbreviations section	Marine

# Introduction
## About the Document
This document describes the key transfer algorithm of Metax. The algorithm is described for the Link layer.
## Terms, Acronyms and Abbreviations
Link – Manages connections with peers
LAN (Local area network) - is a computer network that interconnects computers within a limited area
WI-FI - is a family of radio technologies commonly used for wireless local area networking (WLAN) of devices
network IP (Internet Protocol) – is an IP of a device connected to the network
subnet - is a logical subdivision of an IP network
## References
1. leviathan_whitepaper.odt
2. leviathan_system_overview.odt
3. metax_general_notes.txt
4. leviathan_metax_api.odt
# Key Transfer Algorithm

Device B
Requests the user keys from Device A

Device A
Has user keys

Connected to the same network

For transferring user keys i.e user public/private keys, user json encryption key from Device A to Device B the following steps should be performed:
1. Device A starts pairing mode via start_pairing request. The request has a timeout parameter, which shows seconds count after which the pairing mode will be expired and the request returns a generated code (i.e an alpha-numeric random string containing 7 characters which is supposed to be used by 2 devices as a confirmation that they belong to the same user). The details of start_pairing request are described in [4].
2. Device B requests for user keys from Device A via request_keys request. The request has an ip parameter (to pass Device A ip) and code parameter (to pass the generated code of Device A) and returns whether the transfer of user keys has succeeded or not. The details of request_keys request are described in [4].
If Device B does not have network IP of Device A a functionality is provided to get network IPs of all devices which are in the pairing mode and in the same network via get_pairing_peers request. The details of get_pairing_peers request are described in [4].

Also Device A could stop pairing mode via cancel_pairing request. Details of cancel_pairing request are described in [4].
# Key Transfer Algorithm in Link
Key Transfer algorithm is organized via 4 requests described in Key Transfer Algorithm:
1. start_pairing request
2. cancel_pairing request
3. get_pairing_peers request
4. request_keys request
## start_pairing request in Link
The following functionality is performed:
Returns “Server is already created” error message.
If server socket is already created:

True
Creates a server. If server is created properly:
Returns empty code.
Generates and returns a code. Then starts a timer, which will close the server after specified seconds (timeout is given in request).

False

True

False

## cancel_pairing request in Link
Stops server and timer if they were started during start_pairing request, otherwise does nothing.
## get_pairing_peers request in Link
The following functionality is performed:
1. Gets all network IP addresses and subnet masks of all available(LAN or Wi-Fi) networks of the device.
2. Iterate through all addresses in the same network and get IPs of the devices that are in pairing mode. Returns all those addresses.
## request_keys request in Link
The following functionality is performed:
1. Connects to the server (the ip of the server is given in request).
2. Sends the code (the code is given in request) to server. If the code is correct server sends user public/private keys, user json encryption key sequentially. If the user keys are sent properly the server sends notification “Successfully send keys to <IP>" via 8001 port, where <IP> is the IP of the device which requested the keys.
3. Receives the keys and save in corresponding files.
4. Returns “Receive keys.” message if the keys are saved and “Fail to receive keys.” otherwise.